SITE SPECIFIC RECOMMENDATIONS

EAST REGION:	Central District

LOCATION		Cornell 															Ward 16

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 067 |  | - too many swings | - remove two |  | 1 |  |  |
| 4 Baby |  | - S-hooks | - replace | 10 | 1 |  |  |
|  |  | - improper seats | - replace | 200 | 1 |  |  |
|  |  | - paint chipped | - paint supports | 50 | 2 |  |  |
|  |  | - safety zone | - excavate |  |  |  |  |
| PLG02SSM - 067 |  | - too many swings | - remove two |  | 1 |  |  |
|  |  | - hanger bearings | - invert bolt |  | 1 |  |  |
|  |  | - S-hooks | - replace | 10 | 1 |  |  |
|  |  | - paint chipped | - re-paint supports | 50 | 2 |  |  |
|  |  | -safety zone | - excavate |  |  |  |  |
| PLG03SST - 067 |  | - entanglement | -weld | 50 | 1 |  |  |
| Sr. Straight Slide |  | - barriers | - picket >48” | 200 | 3 |  |  |
|  |  | - safety zone | - excavate |  |  |  |  |
| PLG04SST - 067 |  | - entanglement | - weld | 50 | 1 |  |  |
| Sr. Mogel Slide |  | - barriers | - picket >48” | 200 | 3 |  |  |
|  |  | - improper sides/exit | - replace slide | 2000 | 2 |  |  |
|  |  | - safety zone | - excavate |  |  |  |  |
| PLG05TTM - 067 |  | -too many see-saws, <48” | - remove two |  | 2 |  |  |
| See-Saw |  | -cushioning | - add rubber under seats | 200 | 2 |  |  |
|  |  | -safety zone | - excavate |  |  |  |  |
| PLG06RCM - 067 |  | -safety zone |  |  |  |  |  |
| Rainbow Climber |  |  |  |  |  |  |  |
| PLG07INM - 067 |  | - barriers | - pickets >48” | 300 | 4 |  |  |
| Int. Creative Str |  | - fireman pole <60” | - replace | 100 | 2 |  |  |
|  |  | - improper play spaces | - cap supports | 100 | 2 |  |  |
|  |  | - S-hooks | - replace | 10 | 1 |  |  |
|  |  | - safety zone | - excavate |  |  |  |  |
| Base Material |  |  | -rototill & add base |  | 8 | 990 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| TOTAL COST |  |  |  | 3530 | 49 | 1990 |  |

File Name: K:\PLAY\SCARB\WARD-16\CORNELL.WPD