SITE SPECIFIC RECOMMENDATIONS

NORTH REGION::	Central District

LOCATION 		Cortleigh Parkette	         													Ward 9

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0101SSW3529P |  | -improper spacing | -remove one swing and adjust |  | 1 |  |  |
| 3 Baby Swing |  |  |  |  |  |  |  |
| PLG0201TTW3529P |  | -entrapment between up-rights | -remove |  | 4 |  |  |
| Teeter Totter |  | -pinch & crush points |  |  |  |  |  |
| PLG0301JRW3529P |  | -entrapment in steering wheel | -replace with new plastic wheel | 60 | 1 |  |  |
| Jr. Cr. Structure |  | -no slide barriers | -install barriers | 400 | 8 |  |  |
|  |  | -play surfaces | -cap | 50 | 2 |  |  |
|  |  | -no barriers | -picket rails | 320 | 8 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 | 75 |  |
|  |  | -roots throughout base | -redevelop |  | 16 | 3200 |  |
| Total |  |  |  | 830 | 48 | 3275 |  |

File Name: K:\PLAY\NORTH\WARD-9\CORTLEIG