SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION		Cummer Park	 													Ward 12

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PL60101SSM4002P |  | -non sufficient safety zone | -convert senior to intermediate, reset | 100 | 8 |  |  |
| 4 Senior Swing Set |  | -too many swings | -remove and adjust |  | 1 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -chipped | -repaint | 50 | 2 |  |  |
|  |  | -seat | -replace | 130 | 1 |  |  |
| PL6201SSM4002P |  | -spacing | -adjust |  | 1 |  |  |
| 2 Baby Swing Set |  | -seat pinch shear crush | -replace | 65 | 1 |  |  |
| PL6031JRW4002P |  | -barriers | -replace egress / access | 300 | 4 |  |  |
| Jr. Cr. Structure |  | -play area | -cap pole beams | 100 | 2 |  |  |
|  |  | -X’s & O’s bulb | -replace | 50 | 2 |  |  |
| PL601TTW4002P |  | -hand rail missing | -order and replace | 150 | 2 |  |  |
| Teeter Totter |  | -entrapment | -remove handrails & modify handles | 150 | 2 |  |  |
|  |  |  | -block cover springs & centre hoop | 100 | 2 |  |  |
| PL6401INW4002P |  | -play areas | -cap beams | 150 | 4 |  |  |
| Int. Cr. Structure |  |  |  |  |  |  |  |
| PL6501TAT4002P |  | -none |  |  |  |  |  |
| Talk Tube |  |  |  |  |  |  |  |
| PL607SSP4002P |  | -entrapments | -add / weld backing to stairs | 300 | 4 |  |  |
| Spiral Slide |  | -barriers | -replace 38” high hand rails | 400 | 4 |  |  |
|  |  | -entanglement | -caulk | 10 | 1 |  |  |
| Base Material |  |  | -rototill |  | 8 |  |  |
|  |  |  | -add base 20 T |  |  | 300 |  |
|  |  |  | -excavate |  | 8 | 500 |  |
| Total |  |  |  | 2065 | 58 | 800 |  |

File Name: K:PLAY\NORTH\WARD-12\CUMMER