SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION 		Duncairn Park													                  Ward 11

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0101SSM5512P |  | -seats | -replace | 130 | 1 |  |  |
| 4 Baby Swing Set |  |  |  |  |  |  |  |
| PLG0201SSM5521P |  | -fall height over 11’ | -remove & reset lower | 200 | 24 |  |  |
| 2 Belt Swing Set |  | -safety zone | -prune trees |  | 2 |  |  |
| PLG0301CBG5521P |  | -entanglement | -remove and replace | 1200 | 4 |  |  |
| Billy Goat Climber |  | -entrapment |  |  |  |  |  |
| PLG0401SST5521P |  | -platform requires pickets | -add pickets | 200 | 2 |  |  |
| Straight Slide |  | -entanglement | -in fill |  | 2 |  |  |
|  |  | -protrusions | -remove |  | 1 |  |  |
| PLG0501CHB5521P |  | -entanglement | -remove and replace | 1000 | 6 |  |  |
| Horizontal Climber |  | -protrusions |  |  |  |  |  |
| PLG0601CRC5521P |  | -entrapment | -in fill | 50 | 3 |  |  |
| Rocket Climber |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill and top up 40T |  | 8 | 600 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| Total |  |  |  | 2780 | 61 | 1600 |  |

File Name: K\PLAY\NORTH\WARD-11DUNCAIRN