SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Ellerslie Park															  Ward 10

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PL6101SSW3534P | 1986 | -insufficient safety zone | -excavate, new timber edging, |  |  |  | -site replacement |
| 3 Baby 2 Belt |  |  |  |  |  |  |  |
| PL6201TTW3534P |  | -insufficient safety zone | -relocate |  |  |  |  |
| Teeter Totter |  | -pinch & crush points | -remove |  |  |  |  |
| PL6301JRW3534P |  | -improper barrier, over 3” | -remove guard rails & install picket |  |  |  |  |
| Jr. Cr. Structure |  | -improper steering wheel | -replace |  |  |  |  |
|  |  | -footing showing on chain ladder | -reset footing |  |  |  |  |
|  |  | -no barriers on slide | -install barriers |  |  |  |  |
|  |  | -no grip on climbers | -install grips |  |  |  |  |
| PL6401SRW3534P |  | -tire swing does not meet standard | -remove tire swing |  |  |  |  |
| Sr. Cr. Structure |  | -platforms uneven | -level platforms & adjust footings |  |  |  |  |
|  |  | -access to top of hand to hand | -remove 2 horizontal & 1 vertical bar |  |  |  |  |
|  |  | -rope climber opening too big | -add pickets |  |  |  |  |
|  |  | -insufficient safety zone | -move edging |  |  |  |  |
|  |  | -improper rails on suspension bridge | -remove 4X4’s replace replace floor boards with 2X4 on reverse side |  |  |  |  |
|  |  | -platforms weak | -replace 2X6 |  |  |  |  |
|  |  | -broken support post | -replace support on senior slide |  |  |  |  |
|  |  | -rusted tract ride | -scrape & paint |  |  |  |  |
| PL6401SRW3534P |  | -pinch & crush points on bridge | -anchor bridge |  |  |  |  |
| Con’t |  | -no caps on 6X6 | -install caps |  |  |  |  |
|  |  | -twisted 2X6 on platforms | -replace |  |  |  |  |
| Base Material |  | -compacted | -compacted |  |  |  |  |
|  |  |  | -base material |  |  |  |  |
|  |  |  | -excavate |  |  |  |  |
| Total |  |  |  | 0 | 0 | 0 |  |

File Name: K:\PLAY\NORTH\WARD-10\ELLERSLI