SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	West District

LOCATION 		Fountainhead Park														Ward 7

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM1004P |  | -none |  |  |  |  |  |
| 2 Belt Swing |  |  |  |  |  |  |  |
| PLG02SSM1004P |  | -non sufficient safety zone | -remove 15’ timber, excavate and add sand |  |  |  | -remove garbage container in swing area |
| 2 Baby Swing |  |  | -re-install 20 ft’ timber | 300 | 4 |  |  |
| PLG03TTW1004P |  | -not up to standard | -remove |  | 4 |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG04TAT1004P |  | -none |  |  |  |  |  |
| Talk Tube |  |  |  |  |  |  |  |
| PLG05SRW1004P |  | -entrapment in benches | -remove benches |  | 2 |  |  |
| Sr. Cr. Structure |  | -barriers on straight slides | -install barriers | 100 | 2 |  |  |
|  |  | -trip hazard at entrances | -remove 2X4 |  | 1 |  |  |
|  |  | -pinch point log chain ladder | -refit to under frame |  | 2 |  |  |
|  |  | -no assist handles on climbers | -install four handles | 100 | 2 |  |  |
| Base Material |  | -compacted | -rototill, add base |  | 8 | 600 |  |
|  |  | -non sufficient safety zone | -excavate and add sand |  | 8 | 1000 |  |
| Total |  |  |  | 500 | 33 | 1600 |  |

File Name: K:\PLAY\NORTH\WARD-7\FOUNTAIN