SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	East York District

LOCATION		Gledhill															Ward 1

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -play area | -cap support and beams | 150 | 2 |  |  |
| 2 Belt |  | -encroachment | -relocate swings |  | 8 |  |  |
|  |  | -wood border | -remove |  | 4 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
| PLG02SSM |  | -play area | -cap supports & beams | 150 | 3 |  |  |
| 2 Baby |  | -wood border | -remove |  | 4 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -improper spacing | -adjust |  | 1 |  |  |
| PLG03SRM |  | -barriers | -picket > 48” | 300 | 4 |  |  |
| Sr. Cr. Structure |  | -fireman pole | -make access to 60” | 100 | 2 |  |  |
|  |  | -encroachment | -remove wood border |  | 4 |  |  |
| PLG04SST |  | -encroachment | -remove wood border |  | 4 |  |  |
| Jr. Str.Slide |  |  |  |  |  |  |  |
| PLG05SPR |  | -encroachment | -remove wood border |  | 2 |  |  |
| Four Seat Spring Toy |  |  |  |  |  |  |  |
| PLG06SPR |  | -encroachment | -remove wood border |  | 2 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG07SPR |  | -spring toy missing | -replace | 700 | 4 |  |  |
| Spring Toy |  | -encroachment zone | -remove wood border |  | 2 |  |  |
| Base Material |  | -compacted | -rototill, add base 88T |  | 8 | 1320 |  |
|  |  | -non sufficient safety zone | -excavate |  | 8 | 1500 |  |
| Total Cost |  |  |  | 1420 | 64 | 2820 |  |

File Name: K:\SCARB\WARD-1\GLEDHILL