SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	North District

LOCATION		Littles Road															Ward 18

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 214 |  | -S-hooks | -replace | 10 | 1 |  |  |
| 4 Baby |  | -play area | -cap support & beam | 300 | 4 |  |  |
| PLG02SSM - 214 |  | -tire | -remove tire, add 2 belt | 200 | 4 |  |  |
| 2 Belt , 1 Tire |  | -play area | -cap support & beam | 300 | 4 |  |  |
| PLG03SPR - 214 |  | -handle | -cap end | 10 | 1 |  |  |
| Rocket |  |  |  |  |  |  |  |
| PLG04TTS - 214 |  | -play area | -cone middle | 50 | 2 |  |  |
| Quad Spring Teeter |  |  |  |  |  |  |  |
| PLG05INM - 214 |  | -spiral slide exit | -add 12” <5º | 400 | 4 |  |  |
| Int. Cr Structure |  | -entrapments | -adjust climbers | 20 | 2 |  |  |
|  |  | -barriers | -picket >48 & egress / access | 800 | 6 |  |  |
|  |  | -entanglement | -cover poly slide egress | 50 | 2 |  |  |
|  |  | -play area | -cap support & beams | 400 | 4 |  |  |
|  |  | -steering wheel | -replace with solid | 60 | 1 |  |  |
| Base Material |  | -compacted | -rototill, add base material 66T |  | 8 | 990 |  |
|  |  | -non sufficient safety zone | -excavate |  | 8 | 1500 |  |
| Total Cost |  |  |  | 2600 | 51 | 2490 |  |

File Name: K:\PLAY\SCARB\WARD-18\LITTLES.WPD