SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Ancona Park															   Ward 10

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM3504P |  | -swings <30” from support bars | -adjust to standards |  | 2 |  |  |
| 4 Belt |  |  |  |  |  |  |  |
| PLG02SSM3504P |  | -swings <30” from support bar | -adjust to standards |  | 2 |  |  |
| 2 Baby |  | -improper seats | -replace | 120 | 1 |  |  |
| PLG603SPR3504P |  | -neck entrapment | -replace sides | 100 | 8 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG604INW3504P |  | -barriers | -picket platforms & access/egress >48” | 60 | 8 |  |  |
| In. Cr. Structure |  | -play surface | -replace 4X4’s with 6X2 | 100 | 8 |  |  |
|  |  | -steering wheels | -replace with solid wheel | 60 | 1 |  |  |
|  |  | -non-sufficient safety zone | -remove park bench, cement pad, excavate and add base material |  |  |  |  |
|  |  | -elevated table | -lower |  | 3 |  |  |
|  |  | -neck entrapment on spiral | -new entrance section | 300 | 8 |  |  |
|  |  | -non gripping wood climber | -change to rungs | 100 | 12 |  |  |
| PLG05JRW3504P |  | -no hand grip at double slide | -install rail | 50 | 3 |  |  |
| Jr. Cr. Structure |  | -benches too high | -lower benches |  | 4 |  |  |
|  |  | -play surface on barriers | -cap | 100 | 12 |  |  |
|  |  | -entanglement at slide | -infill | 40 | 4 |  |  |
| PLG06TRM3504P |  | -none |  |  |  |  |  |
| Track Rider |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill and top up |  | 8 | 600 |  |
|  |  | -non sufficient safety zone | -excavate |  | 8 | 1000 |  |
| Total |  |  |  | 1030 | 92 | 1600 |  |

FILE NAME: K:\PLAY\NORTH\WARD-10\ANCONA.WPD