SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Balmoral Park	         													Ward 8

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0101SSW3509P |  | -improper spacing | -remove one swing & adjust |  | 4 |  | -bearings can’t be greased |
| Swing Set (2 Baby) |  | -S-hooks | -replace | 10 | 1 |  | -replace with new |
| PLG01SSP2509P |  | -entanglement at top | -add infill |  | 1 |  |  |
| Int Spiral Slide |  | -protective barriers too high | -change barriers / add infill | 100 | 3 |  |  |
| PLG0201SSW3509P |  | -improper spacing | -remove & adjust other or remove completely |  | 4 |  | -can’t be geased |
| Swing Set 2 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
| PLG02STW2509P |  | -improper spacing | -remove completely |  | 4 |  |  |
| Tire Swing |  |  |  |  |  |  |  |
| PLG03015SPR3509P |  | -none |  |  |  |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG03CUB2509P |  | -none |  |  |  |  |  |
| Chin Up Bars |  |  |  |  |  |  |  |
| Horizontal Climber |  | -access rungs too far apart | -adjust spacing |  | 2 |  |  |
| PLG0401SPR3509P |  | -protrusion | -change foot pegs | 100 | 1 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG0501SRW3509P |  | -2 platforms badly sloped | -reset post | 100 | 8 |  | -replace structure |
| Sr. Cr. Structure |  | -entrapment between pickets | -replace with higher barriers |  |  |  |  |
|  |  | -entrapment between ladder rungs | -construct new ladder | 200 | 8 |  |  |
|  |  | -entrapment throughout new bridge | -replace with new wood bridge | 1000 | 24 |  |  |
|  |  | -improper spacing between fire pole and platform | -install new pole | 200 | 3 |  |  |
|  |  | -vertical rope climbers - wire exposed | -replace with new | 2000 | 6 |  |  |
|  |  | -14 ft. Lin. & post are play surface | -cap or cut | 150 | 3 |  |  |
|  |  | -rope bridge, entrapment | -replace with solid bridge | 150 | 10 |  |  |
|  |  | -guard rails where barriers should be | -install proper barriers |  |  |  |  |
|  |  | -platform plywood deteriorating | -replace | 800 | 12 |  |  |
|  |  | -slide edges splintered | -replace slide | 2000 | 8 |  |  |
|  |  | -stair-handrail too low | -raise & picket | 100 | 6 |  |  |
| PLG0601JRW2509P |  | -entrapment in port holes | -enlarge holes |  | 3 |  |  |
| Jr. Cr. Structure |  | -entrapment between pickets | -add pickets (3) & adjust the rest | 25 | 3 |  |  |
|  |  | -improper spacing between fire pole and platform | -remove and picket | 200 | 2 |  |  |
|  |  | -plywood splintered | -replace sections | 1000 | 10 |  |  |
|  |  | -rope climber worn, wires showing | -replace | 1000 | 6 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 | 600 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| Total |  |  |  | 9145 | 149 | 1600 |  |

File Name: K:\PLAY\NORTH\WARD-8\BALMORAL