SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Centre Park															Ward 10

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSW4514P |  | -too many swings | -remove one baby swing & adjust |  |  |  | -total redevelopment |
| 3 Baby 2 Belt |  | -spacing does not meet standard | -adjust to 30” from support |  |  |  |  |
|  |  | -play surface on top beams | -cap add 2X2 |  |  |  |  |
|  |  | -tree branches encroach | -remove by pruning |  |  |  |  |
|  |  | -inadequate safety zone for belts | -shorten chain 4” |  |  |  |  |
| PLG02TTW4514P |  | -pinch /crush hazard | -remove |  |  |  |  |
| Teeter Totter |  | -protrusion |  |  |  |  |  |
| PLG03JRW4514P |  | -steering wheel | -replace |  |  |  |  |
| Jr. Structure |  | -barriers | -pickets >30” |  |  |  |  |
|  |  | -beams | -replace with <2” with beams |  |  |  |  |
|  |  | -crawl tube head entrapment | -replace |  |  |  |  |
|  |  | -log/chain climber too large for gripping | -replace with metal rungs make 75º |  |  |  |  |
|  |  | -all vertical climber too large for gripping | -replace with metal rungs or similar |  |  |  |  |
| PLG04SRW4514P |  | -tire swing | -remove frame |  |  |  |  |
| Sr. Cr. Structure |  | -barrier | -picket >48” |  |  |  |  |
|  |  | -beams | -replace with <2” width beam |  |  |  |  |
|  |  | -track ride | -remove or relocate |  |  |  |  |
|  |  | -pickets on upper section neck entrapment | -block off entrapment |  |  |  |  |
|  |  | -tube slide has entanglement & entrapment | -remove and replace |  |  |  |  |
|  |  | -flexible bridge - pinch hazard | -immobilize |  |  |  |  |
|  |  | -climbing rungs & log chain too large | -change to metal rungs |  |  |  |  |
|  |  | -rope climber not compliant | -change fasteners & secure below grade |  |  |  |  |
|  |  | -horizontal ladder access too high rungs too far away from platform | -replace ladder, remove access rung |  |  |  |  |
|  |  | -rung ladder less than 75º | -replace or picket or make ladder 75-90 |  |  |  |  |
|  |  | -no in-fill between adjacent platforms | -place in fill |  |  |  |  |
| Base Material |  | -compacted | -compacted |  |  |  |  |
|  |  |  | -base material |  |  |  |  |
|  |  |  | -excavate |  |  |  |  |
| Total |  |  |  | 0 | 0 | 0 |  |

File Name: K:\PLAY\NORTH\WARD-10\CENTRE