SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Debell Lane Parkette													Ward 10

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSW4531P |  | -none |  |  |  |  |  |
| 2 Baby 2 Belt |  |  |  |  |  |  |  |
| PLG02TTW4531P |  | -none |  |  |  |  |  |
| Spring Teeter Totter |  |  |  |  |  |  |  |
| PLG03JRW4531P |  | -barriers | -picket all heights over 30” with proper egress / access | 100 | 6 |  |  |
| Sr. Structure |  | -rails & beams | -route or cut 3 X 6 to 2 X 6 |  | 10 |  |  |
| PLG04SSM4531P |  | -tire does not meet standard | -remove or replace with belt | 130 | 8 |  |  |
| Tire Swing |  | -non sufficient safety zone |  |  |  |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  |  | -add base |  |  | 600 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| Total |  |  |  | 230 | 40 | 1600 |  |

File Name: K:\PLAY\NORTH\WARD-10\DEBELLLN