SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Edithvale Park -  North Playground												Ward 10

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG03TTW3533P |  | -pinch / crush points | -remove and replace | 1500 | 8 |  |  |
| Teeter Totter |  | -protrusions |  |  |  |  |  |
| PLG05SSW3533P |  | -tire swing not up to standard | -remove tire swing and frame |  | 8 |  |  |
| 3 Baby, 1 Tire |  | -improper spacing | -remove one baby swing and adjust |  | 2 |  |  |
|  |  | -non sufficient safety zone | -remove border |  | 3 |  |  |
|  |  | -elevated play surface | -add 2X2 | 10 | 1 |  |  |
|  |  | -entrapment | -in fill | 35 | 2 |  |  |
| PLG06JRW3533P |  | -barriers | - picket all platforms 2 X4’s (22 X 8’) | 300 | 8 |  |  |
| Jr. Structure |  | -retaining wall is too high | -remove ramps & replace with stairs | 400 | 20 |  |  |
|  |  | -elevated play surface | -add 2X2 | 30 | 3 |  |  |
|  |  | -4X4 vertical chain climbers too wide | -change to rungs | 100 | 8 |  |  |
|  |  | -tire climber | -entrapment |  |  |  |  |
|  |  | -no side walls at slide entry | -install | 400 | 8 |  |  |
|  |  | -sand box edge | -remove either side of crawl tube |  | 1 |  |  |
| PLG07SPR4304P |  | -entrapment | -remove and replace | 700 | 2 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG08PLA4304P |  | -non sufficient safety zone | -move border back one foot, | 200 | 6 |  |  |
| Play House |  | -no handrails | -install continuous hand rail | 40 | 4 |  |  |
|  |  | -tires entrapment | -remove and add rails to ramp | 50 | 4 |  |  |
|  |  | -slide edges | -remove inside edge of slide |  | 1 |  |  |
|  |  | -bench is play surface | -remove seat |  | 1 |  |  |
|  |  | -elevated play surface | -add 2X2 | 12 | 2 |  |  |
|  |  | -no bar above slide | -add bar | 20 | 3 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  |  | -base material |  |  | 1200 |  |
|  |  |  | -excavate |  | 8 | 1500 |  |
| Total |  |  |  | 3797 | 111 | 2700 |  |

File Name: K:\PLAY\NORTH\WARD-10\EDITHV-N