SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Flemington (West of Allen Expressway)	         										Ward 8

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0801SSW2524P |  | -improper spacing | -remove one swing and adjust |  | 3 |  |  |
| 3 Baby Swing |  |  |  |  |  |  |  |
| PLG0901TTW2524P |  | -entrapment between 6X6 supports | -fill with 6X6X2 | 200 | 1 |  |  |
| Teeter Totter |  | -pinch & crush points | -remove |  | 4 |  |  |
| PLG10LJRW2524P |  | -entrapment between slides & support | -fill with half sheet stay-white | 200 | 2 |  |  |
| Jr. Cr. Structure |  | -entrapment in old steering wheels | -replace with 2 new wheels | 200 | 1 |  |  |
|  |  | -no slide barriers | -install barriers | 800 | 16 |  |  |
|  |  | -elevated play surface | -cap | 100 | 4 |  |  |
| PLG1101SRW2524P |  | -3 platforms badly sloping | -reset posts | 150 | 16 |  |  |
| Sr. Cr. Structure |  | -entrapment between tube slide & support | -fill with half sheet stay-white | 200 | 4 |  |  |
|  |  | -track ride attached | -remove or relocate |  | 14 |  | -removal |
|  |  | -elevated play surface | -cap | 100 | 4 |  |  |
|  |  | -no grips on climbers | -install rungs | 50 | 7 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 | 1000 |  |
|  |  | -non sufficient safety zone | -excavate |  | 16 | 1200 |  |
| Total |  |  |  | 2000 | 100 | 2200 |  |

File Name: K:\PLAY\NORTH\WARD-8\FLEMINGW