SITE SPECIFIC RECOMMENDATIONS

WEST	REGION:	North District

LOCATION		Gihon Springs Park														Ward 5

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -encroachment zone | -remove / relocate bench |  | 2 |  |  |
| 2 Belt 2 Baby |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -non sufficient safety zone |  |  |  |  |  |
| PLG02DCM |  | -exposed nut threads | -grind the nuts |  | 1 |  |  |
| Dome Climber |  | -non sufficient safety zone |  |  |  |  |  |
| PLG03SST |  | -entrapments: stairs & guardrails | -remove and replace | 2500 | 8 |  |  |
| Sr. Slide |  | -walls too low, entanglement |  |  |  |  |  |
| PLG04SST |  | -non sufficient safety zone |  |  |  |  |  |
| Jr. Slide |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill, add base material 16T |  | 8 | 240 |  |
|  |  | -non sufficient safety zone | -excavate |  | 16 | 1000 |  |
| TOTAL COST |  |  |  | 2510 | 36 | 1240 |  |

File Name: K:\ETOBI\WARD-5\GIHON..WPD