SITE SPECIFIC RECOMMENDATIONS

EAST 	REGION:	North District

LOCATION		Huntsmill															Ward 17

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM - 170 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| 4 Baby |  | -improper seats | -replace | 120 | 1 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -hanger bearings | -replace | 80 | 1 |  |  |
| PLG02SSM - 170 |  | -improper spacing | -remove two, adjust spacing |  | 1 |  |  |
| 6 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
|  |  | -hanger bearings | -replace | 160 | 2 |  |  |
| PLG03BGM - 170 |  | -slide width | -replace slide | 1000 | 4 |  |  |
| Billy Goat Climber |  | -barriers | -add middle rail, add access / egress | 300 | 3 |  |  |
| PLG04SRM - 170 |  | -barriers | -add pickets > 48” | 500 | 6 |  |  |
| Sr. Cr. Structure |  | -fire man pole | -replace | 150 | 2 |  |  |
|  |  | -entrapment | -add access component | 50 | 2 |  |  |
|  |  | -entanglement | -weld |  | 2 |  |  |
|  |  | -slide sides | -replace with double slide | 1500 | 9 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  | -non sufficient safety zone | -add base 88T |  | 8 | 1320 |  |
|  |  |  | -excavate |  |  | 2000 |  |
| Total Cost |  |  |  | 3880 | 52 | 3320 |  |

File Name: K:\SCARB\WARD-17\HUNTSMIL.WPD