SITE SPECIFIC RECOMMENDATIONS

SOUTH REGION:	Central District

LOCATION		Lithuania															Ward 19

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM |  | -improper spacing | -remove one seat, adjust spacing |  | 2 |  |  |
| 3 Belt |  |  |  |  |  |  |  |
| PLG02SSM |  | -improper spacing | -remove two, adjust spacing |  | 4 |  |  |
| 6 Baby |  |  |  |  |  |  |  |
| PLG03TTM |  | -entrapment in handles | -replace handles | 150 | 3 |  |  |
| Spring Teeter Totter |  |  |  |  |  |  |  |
| PLG04SPR |  | -nil |  |  |  |  |  |
| Spring Elephant |  |  |  |  |  |  |  |
| PLG05SPR |  | -protrusions in handle | -remove & replace | 1000 | 4 |  |  |
| Spring Motorcycle |  | -entrapment between wheels |  |  |  |  |  |
| PLG06SPR |  | -entrapment in handles & footrest | -remove & replace | 1000 | 4 |  |  |
| Spring Toy |  |  |  |  |  |  |  |
| PLG07INM |  | -open steering wheel | -replace with solid | 120 | 2 |  |  |
| Jr. Cr. Structure |  | -entrapment between table | -replace panels (4) | 1000 | 8 |  |  |
|  |  | -no drainage in tire climber | -drill holes |  | 1 |  |  |
|  |  | -4 X 4 metal posts (play surface) | -install 6 caps | 100 | 3 |  |  |
| PLG08INM |  | -open steering wheel | -replace with solide | 60 | 1 |  |  |
| Sr. Cr. Structure |  | -top of barrier panels < 2” | -replace | 1500 | 10 |  |  |
|  |  | -entanglement at top of str. slide | -caulk gap | 10 | 1 |  |  |
|  |  | -top of metal posts | -install 17 caps | 250 | 8 |  |  |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  | -non sufficient safety zone | -excavate, add base 7T | 600 | 48 | 105 |  |
| TOTAL COST |  |  |  | 5790 | 107 | 105 |  |

File Name: K:\SOUTH\WARD-19\LITHUANI.WPD