SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION 		Rajah Park	 														Ward 9

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG0101SSW3574P |  | -improper spacing | -remove one swing and adjust |  | 4 |  |  |
| 3 Baby Swing |  | -entrapment between 6 X 6 uprights | -fill with 30’X6”X6” | 100 |  |  |  |
| PLG0201TTW3574P |  | -removed | -replacement required |  |  |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG03SRW2569P |  | -pinch points on log chain and wood climbers | -retro to underside of platforms | 50 | 6 |  |  |
| Sr. Cr. Structure |  | -track ride attached | -remove |  | 2 |  | T.B.D. |
|  |  | -slide barriers | -add barriers | 400 | 8 |  |  |
|  |  | -play surface | -cap | 100 | 8 |  |  |
| PLG0801JRW3574P |  | -2 badly sloped platforms | -rest 6 posts | 700 | 24 |  |  |
| Jr. Cr. Structure |  |  |  |  |  |  |  |
| Base Material |  | -compacted | -rototill |  | 8 | 600 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| Total |  |  |  | 1350 | 68 | 1600 |  |

File Name: K:\PLAY\NORTH\WARD-9\RAJAH.WPD