SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	East District

LOCATION		Saddletree Park														Ward 12

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION |  |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSM4581P |  | -spacing does not meet standard | -adjust to 30” from support at 60” high |  | 2 |  |  |
| 2 Baby |  | -seats | -replace | 130 | 1 |  |  |
|  |  | -S-hooks | -replace | 10 | 1 |  |  |
| PLG02SSM4581P |  | -spacing does not meet standard | -adjust to 30” from support at 60” high |  | 2 |  |  |
| 4 Belt |  | -S-hooks | -replace | 10 | 1 |  |  |
| PLG03JRW4581P |  | -slide egress | add egress hood | 400 | 6 |  | -6 X 2 corey rounded edge |
| Jr Structure |  | -entanglement |  |  |  |  |  |
| PLG04INW4581P |  | -track rider does not meet standard | -remove or replace |  |  |  | T.B.D. |
| Int Structure |  | -barriers | -picket all platforms & egress/access >48 “ | 400 | 8 |  | -6 X 2 metal/greywood |
| Base Material |  | -compacted | -rototill |  | 8 |  |  |
|  |  |  | -base 44T |  |  | 660 |  |
|  |  |  | -excavate |  | 8 | 1000 |  |
| Total |  |  |  | 950 | 37 | 1660 |  |

File Name: K:\PLAY\NORTH\WARD-12\SADDLETR