SITE SPECIFIC RECOMMENDATIONS

NORTH REGION:	Central District

LOCATION		Stafford Park															         Ward 10

| INVENTORY # | BUILT | DEFICIENCIES | RECOMMENDATIONS | COST ESTIMATE |  |  | OTHER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| DESCRIPTION | 1990 |  |  | REPAIRS | LABOUR | BASE | CONSIDERATIONS |
| PLG01SSW3581P |  | -does not meet standards | -remove tire and replace with belt |  | 2 |  |  |
| 3 Baby 2 Belt 1 Tire |  |  | -remove one baby swing & adjust | 100 | 8 |  |  |
|  |  |  | -remove support & re-sink one |  |  |  |  |
|  |  | -non-sufficient clearing | -adjust swings to code | 25 | 2 |  |  |
| PLG02TTW3581P |  | -pinch and crush points | -remove and replace | 1200 | 6 |  |  |
| Teeter Totter |  |  |  |  |  |  |  |
| PLG03JRW3581P |  | -barriers | -2X4 pickets with standard egress/access | 30 | 4 |  |  |
| Jr Structure |  | -designated play surface | -replace 4X4 with 2X4 | 20 | 3 |  |  |
|  |  | -steering wheel unsafe | -replace with solid one | 60 | 1 |  |  |
|  |  | -no barriers on slide | -install barriers | 800 | 16 |  |  |
|  |  | -no grip on climbers | -install grips | 100 | 10 |  |  |
| PLG04SRW3581P |  | -barriers | -2X4 pickets with standard egress/access | 20 | 3 |  |  |
| Sr. Structure |  | -glide rail rusted | -paint | 20 | 1 |  |  |
|  |  | -rung ladder | -remove 4 bars |  | 2 |  |  |
|  |  | -designated play surface | -replace with 2X4 | 30 | 4 |  |  |
|  |  | -4 supports heaved | -re-set supports | 100 | 8 |  |  |
|  |  | -pinch points on bridge | -immobilize | 50 | 6 |  |  |
|  |  | -no in-fill between platforms | -fill space | 50 | 2 |  |  |
|  |  | -no handgrip on climbers | -install grips | 150 |  |  |  |
| PLG04SRW358P |  | -incorrect horizontal rung spacing | -adjust | 50 | 6 |  |  |
| Con’t |  | -sloping platforms | -reset | 200 | 16 |  |  |
| PLG05BBW3581P |  | -none |  |  |  |  |  |
| Base Material |  | -borders, 4 ties are rotten | -replace with 6X6X8 |  | 8 | 200 |  |
|  |  | -compacted | -rototill and add sand |  | 16 | 1600 |  |
| Total |  |  |  | 3005 | 124 | 1800 |  |

File Name: K:\PLAY\NORTH\WARD-10\STAFFORD.WPD